## Slide 1: LAB6 Digital I/O
Mail : p76114391@gs.ncku.edu.tw

## Slide 2: What is “digital I/O”
It is an interface in which each electrical pin may have two states:
  Logical 0 (0V)
  Logical 1 (5V on the basis of the VDD)
Each line can be programmer as:
  an output (lit a LED)
  an input (read a pushbutton)

## Slide 3: Digital Input: Electrical consideration
An input connected to VDD is read (by software) as “1”
An input connected to Ground is read (by software) as “0”
If the input is floating (not connected), the value read cannot be determined!

## Slide 4: Prevent floating state
The typical pull-up resistor value is 1-10kΩ
If in doubt, a good starting point when using a switch is 5kΩ
Disadvantage
  a larger resistance : the input pin responses to voltage changes slower
  a smaller resistance : Too much current flow through

## Slide 5: Prevent floating state
Use pull-up resistor
  Switch open, the value read is “1”
  Switch closed, the value read is “0”

## Slide 6: Prevent floating state
Use pull-down resistor
  Switch open, the value read is “0”
  Switch closed, the value read is “1”

## Slide 7: Bouncing problem
Due to mechanical reasons, pushbuttons and switches(which have a spring inside) typically generate a bouncing signal when pressed or released.
The bouncing signal is read by software ,thus causing malfunctioning

## Slide 8: Button debounce
Hardware solution
  Add a capacitor, in parallel with the button, in order to filter the bouncing signal.
  Reference: http://puppyodie.blogspot.com/2016/04/button-debounce.html
Software solution
  Use delay or interrupt on change function to check input signal again, if the signal stay the same, then considered as press

## Slide 9: Digital Output Electrical consideration
Writing “1” : output high voltage(VDD)
Writing “0” : output low voltage(GND)

## Slide 10: Connecting a LED: calculating the limiting resistor

## Slide 11: I/O ports of PIC18F4520
PIC18F4520 has five I/O ports, called PORTA, PORTB, …, PORTE.
Each port (A-D) has 8 bits and thus 8 electrical pins
Pins are referred as RXY, where X is the port name(A,B,…,E)and Y is the bit number (0, 1, …, 7)
  Ex: RA2→ bit 2 of PORTA
Some pins of the I/O ports are multiplexed with an alternate function from the peripheral features on the device. In general when a peripheral is enabled, that pins may not be used as a general purpose I/O pins.

## Slide 12: I/O ports of PIC18F4520

## Slide 13: I/O ports of PIC18F4520
Each port has 3 registers for its operation. These registers are :
  TRIS register - configure the port as Input or Output
  PORT register - reads voltage of the device
  LAT register - output voltage

## Slide 14: I/O ports of PIC18F4520
TRISx: each bit of this SFR programs the relevant PIN as input or output:
  0 means output
  1 means input
Example:
  TRISC = 0x30 ; // 0x30 = 0011 0000
  RC0 to RC3 → outputs
  RC4, RC5 → inputs
  RC6, RC7 → outputs

## Slide 15: I/O ports of PIC18F4520
LATx: each bit of this SFR programs the output status of the relevant PIN (if it is programmed as output, otherwise it is ignored).
Example:
  LATB = 0xe0; // 0xe0 = 1110 0000
    RB0 to RB4 output 0;
    RB5 to RB7 output 1;

## Slide 16: I/O ports of PIC18F4520
PORTx: each bit of this SFR reflects the input status of the relevant PIN
  If the pin is configured as input, otherwise it replies as the bit of the LATx register
Example:
  Let us read into button variable, the status of the RA5 input pin:
    int button = (PORTA & 0x20); // 0x20 = 0010 0000;

## Slide 17: Features of PORTx register
The RA4 pin is multiplexed with the Timer0 module clock input
Pins RA6 and RA7 are multiplexed with the main oscillator pins
Four of the PORTB pins (RB<7:4>) have an interrupt-on-change feature.
Only pins configured as inputs can cause this interrupt to occur
RB3 can be configured by the Configuration bit, CCP2MX as the alternate peripheral pin for the CCP2 module

## Slide 18: Features of PORTx register
PORTC is multiplexed with several peripheral functions ,like timer1,USART,MSSP
For 40 pin devices, PORTE is a 4-bit wide port
The fourth pin of PORTE (MCLR/VPP/RE3) is an input only pin
RE3 also functions as the programming voltage input during programming

## Slide 19: Bit Field Manipulation in assembly
Single bit manipulation
  BCF f, b, a - clear bit b of register f
  ex: BCF LATB, 0, 0 // will clear LATB bit 0
  BSF f, b, a - set bit b of register f
  ex: BSF TRISA, 5, 0 // will set TRISA bit 5
  BTG f, b, a - toggle bit b of register f
  ex: BTG LATC, 3, 0 // will toggle LATC bit 3

## Slide 20: Bit Field Manipulation in assembly
Multiple bits manipulation
Clear bit: use ANDWF operation
Set bit: use IORWF operation
Toggle bit: use XORWF operation

## Slide 21: Bit Field Manipulation in C
The processor-specific header file includes a structure definition that allows the user to access individual bits of a register
Example
  PORTBbits.RB0 = 1; // pull PORTB bit 0 to high
  LATBbits.LATB0 = 0; // pull LATB bit 0 to low
  TRISBbits.TRISB0 = 0; // pull TRISB bit 0 to low
  STATUSbits.C = 0; // clear the C flag to 0